## Slide 1: EUCLIMIT model consortium: providing analytical input to EU climate policy processes
Lena Höglund-Isaksson
Senior research scholar
Pollution Management Group, Energy, Climate, and Environment Program
International Institute for Applied Systems Analysis (IIASA), Austria
Email: hoglund@iiasa.ac.at

## Slide 2: EU Green Deal (2020) and Fit for 55 legal proposal (2021)
1990=100

## Slide 3: EUCLIMIT consortium model setup: used by EC as analytical basis for developing legal climate proposals (ETS & ESR)
IIASA’s GAINS model contributes non-CO2 scenarios and mitigation cost curves, air pollution impacts
IIASA’s GLOBIOM model contributes CO2 scenarios from Land-use, land-use change and forestry
Macroeconomic projections: JRC and E3modelling (PRIMES model)
Energy & Transport sector projections incl. CO2 emissions: PRIMES model
Agricultural sector projections: CAPRI model (EuroCare, Bonn)
Waste & F-gas use projections:
GAINS (IIASA)
Why model exercise?
Consistency in assumptions across countries
Independent assessment
Trust in fairness of process

## Slide 4: Full consortium project run from Draft to Final (2-3 years cycles) under EC service contracts (since 2010)
1. Updates of input data from latest statistics +model improvements
2. Draft Reference scenario, Technical mitigation potentials and cost curves
3. EC leading Member state and industry stakeholder consultations on Drafts
4. Implementation of feedback from consultations
5. Final Reference and mitigation scenarios and cost curves
EC prepares impact assessment and legal proposals for ETS and ESR national targets, also adding equity aspects to technical assessment
Important features:
Transparency
Timing
Trust
Teamwork across disciplines & models

## Slide 6: Greenhouse gas–Air pollution Interactions and Synergies: The GAINS tool
Policy targets
Social development and economic activities
Emissions
Emission control options: ~2000 measures, co-control of 10 air pollutants and 6 GHGs
Atmospheric dispersion
Costs
Health, ecosystems and climate impact indicators
Optimization

## Slide 7: Non-CO2 sources covered in GAINS

## Slide 8: Current legislation considered in GAINS non-CO2 Draft Reference scenario

## Slide 9: EU27: Baseline non-CO2 emissions

## Slide 10: EU27: Additional non-CO2 mitigation potential
Reduction from 2015:
Baseline: Max:
2030:
non-agriculture: -46% -69%
agriculture: -6% -26%
total: -26% -47%
2050:
non-agriculture: -66% -87%
agriculture: -10% -36%
total: -37% -61%